## Slide 1: 5G NR Device Testing Challenges & Opportunities

## Slide 2: Enabling the Leading-Edge Technology
Device Validation Test
Live Test
Production System Level
Reverse Logistics
  Standards Based
    3GPP  Global Certification Forum
    GSMA
    CTIA
  Mobile Network Operator Conformance
  Device Stability and Stress
  Live Network and Device Interoperability
  Production line and repair center
Automating Tests Across Device Life Cycle and Standards
Notes: For FR2 conformance can only be demonstrated using over-the-air (OTA) testing in far-field conditions. Indirect far-field methods — for example, compact antenna range systems — are possible, but this relies on proving their equivalence with far-field techniques. A further issue is the use of dynamic beamforming antennas in this frequency range to overcome high path loss and line-of-sight blockage. Representing these spatial characteristics in an emulated lab test scenario represents a new challenge compared with existing test methods.
Massive MTC: focus is on coverage, low power consumption, optimized signalling for the massive number of devices to connect, and especially on security. Different challenges of testing.
URLLC: 5G NR provides low-latency support with high sub-carrier spacing, requiring short symbols, self-contained sub-frames, and mini-slot operation. Reliability can be improved with redundancy, and 3GPP 5G NR brings new options for dual connectivity: either EUTRAN + 5G NR dual connectivity or 5G NR dual connectivity. Requirements in these use cases are demanding and potentially extreme. To ensure that vehicle steering systems, M2M communications, or industrial control systems function smoothly, their networks may have to handle incredible amounts of data and do so virtually in real time, so test requirements will be tighter, requiring more accurate verification processes.
OTA testing entails several different challenges including repeatability, configuration, and coverage. Several companies have put forth proposals to address these test challenges but questions remain in terms of accuracy, test time, and ultimately cost. Whatever is included in the RAN4 documents, 5G components and devices must be tested differently with new techniques and technologies from their 4G predecessors.
Beamforming and other mmWave applications create test challenges, as engineers must conduct static tests on devices and antennas in active beam forming environments. Need to optimize the test environment and have to be pragmatic in order to maintain test costs under control.
Traditionally, two test chambers—the reverberation chamber and the more-expensive anechoic chamber—are used when performing OTA measurements. Studies indicate that better results are achieved by conducting far-field measurements (FFM) on mmWave designs. Using this as a basis, OTA measurements will have to be taken 1.5 m to 2 m on devices supporting 28 GHz. That will require a significant investment, as the test chambers would be considerably larger than those currently used for LTE.

## Slide 3: W2BI Product Portfolio for IoT and 5G NR Testing
  QuiNS – Device Conformance
  MLT 1600 GSM/WCDMA/LTE/CAT-M1/NB-IoT
  QuikStress – Mobile Application and Device Stability Testing
  MLT 2000 5G NR Sub-6GHz
  MLT 5G NR - mmWave
Notes: For FR2 conformance can only be demonstrated using over-the-air (OTA) testing in far-field conditions. Indirect far-field methods — for example, compact antenna range systems — are possible, but this relies on proving their equivalence with far-field techniques. A further issue is the use of dynamic beamforming antennas in this frequency range to overcome high path loss and line-of-sight blockage. Representing these spatial characteristics in an emulated lab test scenario represents a new challenge compared with existing test methods.
Massive MTC: focus is on coverage, low power consumption, optimized signalling for the massive number of devices to connect, and especially on security. Different challenges of testing.
URLLC: 5G NR provides low-latency support with high sub-carrier spacing, requiring short symbols, self-contained sub-frames, and mini-slot operation. Reliability can be improved with redundancy, and 3GPP 5G NR brings new options for dual connectivity: either EUTRAN + 5G NR dual connectivity or 5G NR dual connectivity. Requirements in these use cases are demanding and potentially extreme. To ensure that vehicle steering systems, M2M communications, or industrial control systems function smoothly, their networks may have to handle incredible amounts of data and do so virtually in real time, so test requirements will be tighter, requiring more accurate verification processes.
OTA testing entails several different challenges including repeatability, configuration, and coverage. Several companies have put forth proposals to address these test challenges but questions remain in terms of accuracy, test time, and ultimately cost. Whatever is included in the RAN4 documents, 5G components and devices must be tested differently with new techniques and technologies from their 4G predecessors.
Beamforming and other mmWave applications create test challenges, as engineers must conduct static tests on devices and antennas in active beam forming environments. Need to optimize the test environment and have to be pragmatic in order to maintain test costs under control.
Traditionally, two test chambers—the reverberation chamber and the more-expensive anechoic chamber—are used when performing OTA measurements. Studies indicate that better results are achieved by conducting far-field measurements (FFM) on mmWave designs. Using this as a basis, OTA measurements will have to be taken 1.5 m to 2 m on devices supporting 28 GHz. That will require a significant investment, as the test chambers would be considerably larger than those currently used for LTE.

## Slide 4: Multitude of Possibilities for 5G NR Testing
Broad usage scenarios
Dynamic environment
Synchronization, Error Correction
Flexibility PHY parameterization
Real-time processing
Beam Management
NSA & SA
Radiated & conductive
mMTC
eMBB
URLLC
Notes: For FR2 conformance can only be demonstrated using over-the-air (OTA) testing in far-field conditions. Indirect far-field methods — for example, compact antenna range systems — are possible, but this relies on proving their equivalence with far-field techniques. A further issue is the use of dynamic beamforming antennas in this frequency range to overcome high path loss and line-of-sight blockage. Representing these spatial characteristics in an emulated lab test scenario represents a new challenge compared with existing test methods.
Massive MTC: focus is on coverage, low power consumption, optimized signalling for the massive number of devices to connect, and especially on security. Different challenges of testing.
URLLC: 5G NR provides low-latency support with high sub-carrier spacing, requiring short symbols, self-contained sub-frames, and mini-slot operation. Reliability can be improved with redundancy, and 3GPP 5G NR brings new options for dual connectivity: either EUTRAN + 5G NR dual connectivity or 5G NR dual connectivity. Requirements in these use cases are demanding and potentially extreme. To ensure that vehicle steering systems, M2M communications, or industrial control systems function smoothly, their networks may have to handle incredible amounts of data and do so virtually in real time, so test requirements will be tighter, requiring more accurate verification processes.
OTA testing entails several different challenges including repeatability, configuration, and coverage. Several companies have put forth proposals to address these test challenges but questions remain in terms of accuracy, test time, and ultimately cost. Whatever is included in the RAN4 documents, 5G components and devices must be tested differently with new techniques and technologies from their 4G predecessors.
Beamforming and other mmWave applications create test challenges, as engineers must conduct static tests on devices and antennas in active beam forming environments. Need to optimize the test environment and have to be pragmatic in order to maintain test costs under control.
Traditionally, two test chambers—the reverberation chamber and the more-expensive anechoic chamber—are used when performing OTA measurements. Studies indicate that better results are achieved by conducting far-field measurements (FFM) on mmWave designs. Using this as a basis, OTA measurements will have to be taken 1.5 m to 2 m on devices supporting 28 GHz. That will require a significant investment, as the test chambers would be considerably larger than those currently used for LTE.

## Slide 5: Opportunities for 5G NR Testing
End-to-end full automation
Multi-Purpose
Agile system (RF, Core, Apps)
  For NSA – Coexistence of LTE & 5G NR
Scalable
Modular system
Standardized interfaces
Evolved Packet Core - NSA
Test Management
Cloud
Application Servers: DNS, FTP/HTTP, IMS Server, SIM OTA Server, Streaming …
Cloud Services: Reporting, UE Profiles, Licenses, User Management …
LTE
5G NR <6Ghz
5G NR mmWave
eNodeB
gNodeB
PHY
PHY
PDCP, RLC, MAC
New Core Network (5GC) - SA
Notes: The conceptual architecture shown is for the NSA.
As complexity of the system increases in order to maintain the economic viability of the products being released the tests have to be cost controlled (i.e. reduced quantities and times). End device applications will also drive the level of testing where the URLLC would need tighter testing (e.g. 1ms latency) compared to massive IoT.
Reducing the testing costs will play a key role in the success of 5G. If there isn’t a compelling business case to deploy 5G services, the technology may not roll out as expected. To control test costs, engineers must make the decision as to which tests need to be done in an OTA chamber. Chipset, device, and carriers all must agree on an acceptable margin of error for certain performance parameters to eliminate the need for some OTA tests. For example, there will be a considerable amount of protocol tests that will need to be performed. Because verifying the protocol stack does not require RF measurements, protocol testing may be done without a chamber.